# Specific requirements
ID	Name	Description	Prio.
External interface requirements
System Interfaces
1	NMEA Protocol	The well-known NMEA 0813 protocol is used for outputting data from the system.	1
2	NMEA Update	Each Sentence is issued every second.	1
3	NMEA serial configuration	The standard NMEA serial configuration is supported, which is 4800 b/s (bit per second rate) with 8 bits of data, no parity, and one stop bit.	1
4	NMEA speed	Higher baud rates are supported: 9800 b/s and 115200 b/s	2
5	RMC Sentence	The RMC Sentence with all parameters is provided. The data is compiled as follows, where the units are according to the NMEA specs: / Time of fix is the current UTC / Navigation receiver warning is A (valid) when the currently estimated CEP is less than the specified CEP, V (Warning) otherwise. / Latitude and direction is according to the current position estimate / Longitude and direction is according to the current position estimate / Speed over Ground (in Knots!), is current speed estimate / Track angle in degrees is the current track estimate / Date is the current date / Magnetic variation is set to zero / The checksum is calculated according to the data.	1
6	GGA Sentence	The GGA Sentence with all parameters is provided. The data is compiled as follows, where the units are according to the NMEA specs: / Time of fix is the current UTC / Latitude and direction is according to the current position estimate / Longitude and direction is according to the current position estimate / Fix Quality indicator. It is set to: 0 (invalid) when no positioning information was yet obtained since system start. 1 (GPS fix) if a fix from the GPS input was available within the last 3 seconds. 6 (estimated) otherwise / Number of satellites is set to: to the number of satellites from the last GPS fix, if it is not older than 3 seconds, 0 otherwise. / Horizontal dilution of position is set to an estimation of the CEP of the current position estimate. / Altitude, Meters, above mean sea level is set to the value of the last GPS input / Height of geoid (mean sea level) above WGS84 ellipsoid is set to the corresponding value of the last GPS input / time in seconds since last DGPS update is left empty / DGPS station ID number is left empty / The checksum is calculated according to the data.	3
User Interfaces
7	GUI not mandatory	The system must also work (with accordingly limited precision) with no user input at all.	1
56	GUI English	The language of the GUI of the system is US English.	1
	GUI translatable	The language of the GUI can be changed without recompilation, e.g. by replacing one or more files.	1
Selecting the current railway segment
8	GUI railway segment number	At any time, the user may input the railway segment number he or she is currently traveling on. This narrows down the possible positions to a set of lines between the way points for this segment.	1
9	GUI segment as text	The input is possible via a text field.	1
10	Track db input matching	If the input does not match to an entry in the track database, an error message is shown to the user.	1
11	Track db input plausibility	A plausibility check against the current position is done for this user input.	3
12	Track db input success	A successful input of a segment number (re)populates the event marker list. As long as the user has not entered a valid segment number, the event marker list remains empty, thus disallowing firing of event markers.	1
Event marker firing by the user
13	Event firing	The user must be able to fire an event when traveling past a landmark in the event marker database.	1
14	Stop event	The user has the possibility to fire an event, when the train is completely stopped.	1
15	Event list scrollable	The event markers are presented in a scrollable list. Each list entry equals to one event marker.	1
16	Event list population	After the list gets populated (see above), the first event marker is selected.	2
17	Event reselection	When the user fires an event marker, the next one in the list is automatically selected.	2
53	Event shortcut	Firing the selected event marker is possible using a single shortcut key on the computer keyboard.	2
54	Event double-click	Firing an event marker is possible by a double-click of the mouse pointer on an event marker in the list.	1
18	Event re-firing	The system allows a given event marker to be fired more than once. This allows a user to somewhat “correct” a previously executed firing which was too early.	2
19	Last event	If the last event marker in the list was fired, no entry is selected.	2
Status output
20	Status at any time	At any time, the user can see status information of all attached position providers.	2
21	Position Provider Status information	Each position provider provides the following status information: a free textual description (e.g. “3 Satellites in view”), a standard deviation for the last known position, the timestamp of the last known position, and a status indication from one of the following states. / Working:The provider has issued a new position in the last 3 seconds. / Ready:The provider is ready to provide positioning information. / Faulty:The provider is not able to provide positions, because of an error.	2
22	Output status information	At any time, the user can see status information of the currently outputted, estimated position. The status information is the same as for a position provider, respectively.	1
Hardware Interfaces
23	Comport Adapter	For the serial RS-232 interface output, a USB-To-RS-232 Adapter shall get used, if the computer does not have a built-in interface.	1
57	Virtual Comport	The NMEA data is additionally outputted via a virtual com port.	3
Operations
System start and shutdown
24	Engine start	The user starts the system by starting an engine executable file. No other user action is necessarily needed. This step must be automatable at startup of the underlying operating system by a batch file or similar means.	1
25	GUI start	The user starts the graphical user interface via another executable file, as he or she sees necessity for.	2
26	GUI stop	Terminating the user interface does not stop the system's engine executable.	2
27	Engine stop	The user stops the system by terminating the engine executable's process.	1
Functions
Using WiFi as a position provider
28	WiFi scan	The system shall scan for surrounding WiFi access points.	2
29	WiFi lookup	The system shall look up the found access points in a local database with positions of known Access points. If matches are found, the current position of the system shall be estimated by using simple mathematical algorithms.	2
Using GPS as a position provider
30	GPS usage	The system shall use a GPS device.	1
Using an IMS as position provider
31	IMU usage	The system shall use an inertial measurement unit to continue providing position estimate when all other technologies provide no position estimate.	1
Using a track database for correction
32	Track db usage	Before outputting, the system shall tie all estimated positions to the nearest point on a given set of tracks.	1
33	Track as waypoints	The tracks are defined by waypoints.	1
34	Unique segment number	Each track has a unique segment number for identification.	1
35	Segment narrowing	The set of tracks is narrowed down according to user input of the current track segment number	1
Using event markers as position provider
36	Using event markers	The system shall use the event markers fired by the user as positioning data.	1
Logging
37	Log output	The system produces a log of all outputted data.	1
38	Log disabling	Disabling this function must be possible by configuration.	1
39	Log file	The log is written to a file. The filename contains a timestamp of the current UTC time when the log was started.	1
40	XML log	The log file is in a variety of an XML format.	2
Estimating the position
41	Blending inputs	The positioning data gathered from the positioning providers, the IMU, and from the track database is blended together.	1
42	Position estimation	The blending is done in a way that, at any time, the most probable position is outputted, using basic mathematical algorithms.	1
43	Estimation CEP	The CEP after blending is 25 meters or below when the train is stopped, at any time.	3
Performance Requirements
44	Waypoint count	The system is capable of working with as much as 100000 track waypoints.	1
45	AP count	The system is capable of working with as much as 100000 stored access points.	2
46	Maximum speed with GPS	The system works at traveling speeds up to 200 km per hour, when the GPS sensor is providing position estimates.	1
64	Maximum speed with any sensor	The system works at traveling speeds up to 200 km per hour, when any of the sensors is solely providing position estimates.	3
Database requirements
47	Db update	When the system is not running, all data for the track waypoints, the WiFi Access points, and the event markers is replaceable.	2
Design constraints
48	Using laptop	The system runs on a standard, mid-class, laptop computer of a recent date.	1
49	Using 3rd party libs	Used 3rd party components and its interfaces must be noted. In case they do not allow commercial usage through their licensing model, they must be later replaceable and the interfaces used must be described.	1
55	Engine separated	The system has the positioning engine (without any GUI) and the GUI in separate executables.	2
63	Emulation mode	One or more position provider can get emulated to the system with some form of prepared position estimates. This serves for the test of parts of the system without using the actual hardware or boarding a train. An interface for implementation is provided for this.	1
Standards compliance
50	NMEA output	The output conforms to the NMEA 0813 protocol	1
Software system attributes
Source Code
51	Coding Guidelines	The coding guidelines of the customer are applied.	1
Availability
52	Availability	The system must be able to run 10 hours continuously.	2
Other requirements
58	Quick Start Guide	A “Quick Start Guide” of 2 pages A4, laminated is provided in English and German. No further user manual is required.	1
59	Documentation	A documentation according to the needs of the Master Thesis is provided.	1
Accuracy determination
60	GPS Accuracy	The accuracy when using GPS and the track database alone, in open sky conditions, in an ICN2000 car, while the train is stopped, is determined.	2
61	WiFi Accuracy	The accuracy when using WiFi and the track database alone, when at least 3 Access Points are visible, in an ICN2000 car, while the train is stopped, is determined.	2
62	Inertial Accuracy	The accuracy when using inertial measurements and the track database alone, when the train is stopped, is determined, one minute after one of the position providers provided an estimate. This may get simulated in the office without actually boarding a train.	2
65